## Slide 1: Assignment Project Traffic Light using STM32F103RB

## Slide 2: Introduction
In this project, the STM32F103RB is used to simulate the 2-way traffic light system, having some main features:
  Automatic mode: The system operates as normal. The light colors are red, yellow, and green.
  Manual mode: A button is used to switch the light colors in this mode
  Tuning mode: This mode is used to modify the light timing length
  Pedestrian scramble: when the button for pedestrian is pressed, its light is turned on and operates reversely to the light of vehicles

## Slide 3: Block Diagram
Traffic Light 1
(D2 – PA10
D3 – PB3)
Traffic Light 2
(D4 – PB5
D5 – PB4)
Pedestrian Light
(D6 – PB10
D7 – PA8)
Pedestrian Buzzer
(D12 – PA6
TIM3-CH1)
Pedestrian Button
(A0 – PA0)
SELECT
Button
(A1 – PA1)
MODIFY
Button
(A2 – PA4)
SET
Button
(A3 – PB0)
USART2

## Slide 4: Configuration
Clock: 64MHz
TIM2: PSC = 7999, ARR = 79 => 100Hz clock
TIM3 - PWM: PSC = 63, ARR = 999 => 1kHz clock
USART2, baud rate: 9600